## Slide 1
MAGNETIC RESONANCE IMAGING: SEMPER INCITARE
E. Mark Haacke, Ph.D.
Wayne State University
Detroit, Michigan, USA
Ruijing Hospital, SJTU
Shanghai, China

## Slide 2: The Excitement of MRI
Richard Ernst summarized the excitement and future potential of MRI in his 1991 Nobel Prize acceptance speech:
“I’m not aware of any other field of science outside of magnetic resonance that offers so much freedom and opportunity for a creative mind to invent and explore new experimental schemes that can be fruitfully applied in a variety of disciplines.”
The incredible flexibility of MRI is due to the fact that many if not most of the new developments can build on top of the current technology making it more and more powerful.
For example, a sequence can have: multiple echoes, shared k-space, partial Fourier, elliptical sampling, flow compensation gradients, parallel imaging or compressed sensing, diffusion or flow encoding gradients, be interleaved doubling the number of modifications that can be made, etc., etc., etc.

## Slide 3: Education: A labor of Love
“It’s easy to show that …”
Create a text that carries the student step by step through the basic to advanced concepts without once using that phrase!
The result of this 28 man-year effort was “The Green Bible of MRI”.

## Slide 4: The Anatomy Lesson of Dr. Nicolaes Tulp: Rembrandt 1632
In the old days, we cut open the human body from the outside in. Now we look at the body from the inside out.
A budding mathematician
counting his fingers.

## Slide 5: Visualizing Quantum Mechanics
Thin slice T1 and T2 weighted 3D images of the brain. Nobel prize in Medicine or Physiology 2003.
Lauterbur
Mansfield

## Slide 6: Nearly everything you need to know about MRI is buried in the phase information.
E. Mark Haacke, PhD
Wayne State University
Ruijin Hospital, SJTU

## Slide 7
Fundamentals
Basics of gradient-echo signal formation
Phase and its fundamental role in imaging
Phase as a source of T2* dephasing
Background phase/field removal

## Slide 8
Applications
Water/fat separation
Flow quantification
Temperature mapping
Susceptibility weighted imaging (SWI)
Quantitative susceptibility mapping (QSM)
Measuring and visualizing conductivity

## Slide 9: Very basics of the MR scanner
schematic of MR scanner parts - Search

## Slide 10: Magnetic Resonance Imaging
Although quantum physics was needed to formulate the theoretical concepts and explain the experimental design and results in magnetic resonance, the final impact rests on the very simple relationship given by the well known Larmor equation relating the frequency of rotation or precession frequency (w) and the local magnetic field (B) via w = gB.
Larmor equation: w = gB
In vector notation: w = -gB

## Slide 11: Visualizing Quantum Mechanics
Thin slice T1 weighted and thick slice T2W images

## Slide 12: Basic MRI concepts
 = -B
 : the gyromagnetic ratio of the proton 
B: the applied magnetic field
: the magnetic resonance
frequency

## Slide 13
A cylindrical object in a constant magnetic field.
Its bulk magnetization lies parallel to the main field.
rf
G
Signal
t
M0
z
x
y
What happens when an object is inside the magnet?
A simple sequence diagram showing no application of rf or gradient fields and hence no signal.
0
Boz

## Slide 14
Applying an oscillating radiofrequency (rf) field along the x-axis rotates M0 from the z-axis into the transverse plane so that it lies along the y-axis.
M0
Beff
z
x
y
What happens after we apply an oscillating rf field?
M0
Boz
At this time, the rf field is turned off and the transverse magnetization precesses about the main field B0.

## Slide 15: MR Signal Readout
The precessing transverse component induces a voltage in a coil which is placed so that it sees a changing magnetic flux.

## Slide 16: From magnet to console

## Slide 17
Applying an oscillating radiofrequency (rf) field along the x-axis rotates M0 from the z-axis into the transverse plane so that it lies along the y-axis.
Sequence diagram
M0
Beff
rf
G
Signal
t
z
x
y
What happens after we apply an oscillating rf field?
M0
Boz

## Slide 18: Gradient Echoes and 1D Imaging
0
Bz(x)
x
x
ρ(x)

## Slide 19: The Larmor equation
  Right-handed system
  : gyromagnetic ratio.
  For hydrogen,
   = /2π=42.576 MHz/T

## Slide 20: Jump into the rotating reference frame
= 

## Slide 21
By purposely adding a gradient field G, we can spatially distinguish the spins by their frequency content since now
(x) = g (B0 + Gxx)
rot(x) = gGxx
ΔB = Gxx
rf
Gx
Signal
t
t1
t2
z
x
y
Adding a magnetic field gradient to encode spins.
z
Bz
B0
0
ΔBz(x)= -Gzx

## Slide 22
z
x
y
rf
Gx
Signal
t
t1
t2
TE
Applying a dephasing gradient followed by a rephasing gradient causes the spins to first run away from each other and then to turn around and run back creating a gradient echo.
Adding a magnetic field gradient to encode spins.
z
Bz
B0
0
ΔBx(x)= Gxx
Notes: Slide 18

## Slide 23
0
Bz(x)
x
x
ρ(x)
(x) = gGxx

## Slide 24
rf
Gx
Signal
t
t1
t2
TE
Applying a dephasing gradient followed by a rephasing gradient causes the spins to first run away from each other and then to turn around and run back creating a gradient echo.
Adding a magnetic field gradient to encode spins.
x
Bz
B0
0
ΔBz(x)= Gxx
0
Bz(x)
x
x
ρ(x)
t3
Notes: Slide 18

## Slide 25: The MR Signal as a Fourier Transform
where r(x) is the spin density and using k = Gt as the spatial frequency we find
the spin density can be reconstructed as
z
x
y
x
y

## Slide 26: Gradient coil components

## Slide 27: Phase Evolution
Phase is the integral of precession frequency (or field strength) over time
Gradients
Susceptibility Induced Fields
Eddy Currents
Main Field Inhomogeneities
Molecular Environment (Chemical Shift)

## Slide 28: Phase from a Gradient-echo Signal
1Magnitude Image
Phase Image
1Data were acquired using 3D gradient-echo sequence with full flow compensation (SWI sequence).
The complex MRI signal has both real and imaginary components or magnitude and phase components
φ(TE) = γΔB∙TE+φ0, for a left-handed system.

## Slide 29: Insight comes with knowledge
The more you read, the more you discuss, the more you practice, the more you teach, the more insight you will gain.
Sometimes this insight will lead to inspiration, which can come when you least expect it, like waking up in the morning, or taking a long philosophical walk in a beautiful Suzhou garden.

## Slide 30: Pause