## Slide 1
MAGNETIC RESONANCE IMAGING: SPINS, SPINS and yet more SPINS
E. Mark Haacke, Ph.D.
Ruijin Hospital, SJTU, SOM
Wayne State University
Detroit, Michigan, USA

## Slide 2: IMAGING PROTONS WITH MRI
Protons are spin ½ particles.
This means that when you put a proton in a magnetic field it will either be parallel to or anti-parallel to the main magnetic field.

## Slide 3: IMAGING PROTONS WITH MRI
0
0
1
Bo
Spin-1/2 state: its
up or down
In this schematic, there is only 1 excess spin that is parallel to the main field Bo.

## Slide 4: SPIN EXCESS: WHY MRI IS A VERY INEFFICIENT IMAGING MODALITY
only 1 in 106 spins remains pointing up
Bo = 0.15T
In this schematic, there is only 1 excess spin that is parallel to the main field Bo.
5 x 105
-5 x 105

## Slide 5: SPIN EXCESS AT 1.5T
Now there are 10 excess spins parallel to the main field Bo.
Bo = 1.5T

## Slide 6: SPIN EXCESS DEPENDS ON MAGNETIC FIELD
Each spin has its own magnetic moment.
=
M = bulk magnetization
M
1026 in the human brain (1.5L) so the spin excess is 1021

## Slide 7: MRI FREQUENCEY DEPENDENCE ON FIELD: THE LARMOR EQUATION
ω = γBo
This equation has the simplest possible mathematical form a = bc and much of MRI can be understand from its implications.

## Slide 8: WHAT IS FREQUENCY
ω = γBo
Angular frequency is the rate of rotation around an axis of rotation in radians per second (or in degrees per second).
ω = 2πf
Frequency is the rate of rotation around an axis of rotation in cycles per second.

## Slide 9: WHAT IS PHASE
φ = ωt = γBot
Angular frequency is the rate of rotation around an axis of rotation in radians per second (or in degrees per second).
φ = 2πft = 2πγ Bot where
γ = γ/2π
Frequency is the rate of rotation around an axis of rotation in cycles per second.

## Slide 10: WHAT IS PHASE
f = γBo
γ = γ/2π = 42.6 MHz/T
at 1T: f = 42.6 MHz
at 1.5T: f = 64 MHz
at 3T: f = 128 MHz
at 5T: f = 213 MHz
at 7T: f = 300 MHz
at 9.4T: f = 400 MHz
at 11.7T: f = 500 MHz

## Slide 11: ANGULAR DISTANCE = PHASE
Consider the simple process of walking along a sidewalk straight.
What distance (d) have you walked in a time t?
d = vt
In the same way, phase or “angular distance” is
φ = ωt

## Slide 12
φ = ωt
ANGULAR DISTANCE = PHASE
φ0 = 0
ω = 360o per minute or
ω = 2π radians per minute
φ1
φ2
φ0
φ1 = 90o or π/2
φ1 = 180o or π
LHS

## Slide 13
φ = ωt
ANGULAR DISTANCE = PHASE
φ0 = 0
ω = 360o per minute or
ω = 2π radians per minute
φ1
φ2
φ0
φ1 = -90o or -π/2
φ1 = -180o or -π
RHS

## Slide 14
ANGULAR DISTANCE = PHASE
For a left handed system clockwise is positive

## Slide 15: LEFT HANDED
side view
top view
z
y
x

## Slide 16: RIGHT HANDED
side view
top view
z
y
x

## Slide 17
6°TE=7.5ms
6°TE=15ms
6°TE=22.5ms
Magnitude
Phase
AS ECHO TIME CHANGES PHASE CHANGES:
φ = ωTE

## Slide 18: ANGULAR DISTANCE = PHASE
φ = 2πft with f = 1/6 cps

## Slide 19
φ = ωt
ANGULAR DISTANCE = PHASE
φ0 = 0
ω = 360o per minute or
ω = 2π radians per minute
φ1
φ2
φ0
φ1 = -90o or -π/2
φ1 = -180o or -π
RHS

## Slide 20
27°TE=7.5ms
27°TE=15ms
27°TE=22.5ms
Magnitude
Phase
AS ECHO TIME CHANGES PHASE CHANGES:
φ = ωTE

## Slide 21: Size of the magnitude vector does not affect the phase
Note that the phase does not depend on the magnitude of the vector, whether the yellow one or green longer one, they have the same phase.
x
y
z

## Slide 22
AS ECHO TIME CHANGES PHASE CHANGES:
Two flip angles give the same phase image,
despite having totally different signals at each pixel.
TE=7.5ms
TE=15ms
TE=22.5ms
Phase 6o
Phase 27o

## Slide 23: SUMMARY
Spin excess depends on field strength.
The higher the field the bigger the magnetization.
The higher the field the faster the spins precess.
The handedness does not change the physical rotation of the spins only the sign that you assign it.
Phase depends on magnetic field not the image magnitude.

## Slide 24: Pause